## Slide 1: My First steps in Slit spectroscopy
BAAVSS Spectroscopy Workshop
Norman Lockyer Observatory October 2015
Andrew Wilson

## Slide 2: Overview
My choice of spectrograph, camera and telescope
Getting started and basic processing
Some of the problems I’ve overcome
More advanced processing
Interspersed with examples of my spectra

## Slide 3: Spectrographs I’ve Used
Littrow Spectrographs - L200 & LHIRES III
Both use interchangeable diffraction gratings

## Slide 4: SHEYAK INSTRUMENTS LHIRES III
LHIRES III – Littrow Configuration
LHIRES III user manual

## Slide 5: L200
Ken Harrison design built by JTW
Multiple gratings
Optimised for R3000 = 2 Angstroms at H-Alpha

## Slide 6: LHIRES III
Multiple gratings
Optimised for R17000 = 0.35 Angstroms at H-Alpha
Shelyak Instruments

## Slide 7: Camera Choice
Imaging camera
  Starlight Xpress SXVR-H694
    Black and white
    Cooled
    High sensitivity
Guide camera
  Starlight Xpress Lodestar
    Sensitive
    Low noise
    Light

## Slide 8: My Old Observatory
14” F10 Meade
AP1200 GTO

## Slide 9: My New Observatory
10” F8 RC
AP1200 GTO

## Slide 10: Preparation
First of all practice in daylight and indoors
  A good idea to note the micrometre readings for different lines
Spectroscope setup (check at telescope)
  Focus the guide camera on the slit
    May only need to do once
  Select the wavelength
  Focus main camera using the neon spectrum

## Slide 11: At the Telescope
Focus the telescope on a star
  Can do by looking at the guide star image
  Refine by looking at the spectrum and focus until counts or signal are highest
  May need to nudge star back and forth to centre on slit
Test spectrum to make sure everything is OK

## Slide 12: Align Spectra Camera Horizontal Axis
Not aligned (Castor H-alpha at high resolution)
Aligned (CH Cygni at low resolution)

## Slide 13: Locating the Star
Planetarium software
BAAVSS
Charts

## Slide 14: An imaging run – Getting the spectra
Target star
  Find the target star
  Take a neon spectrum
  Position the star on the slit
  Track the telescope on a guide star
  Take star spectrum images
  If long run then take another neon spectrum

## Slide 15: Processing a Spectrum Basic Processing
Calibrate all the images
  Dark frames
  Bias frames (if required)
  Hot pixel removal
Combine the images
Correct spectra for “tilt” and “slant”
Wavelength calibrate the spectrum

## Slide 16: Kappa Cassiopeia
NASA

## Slide 17: Kappa Cassiopeia Low Resolution – No Response Correction

## Slide 18: Kappa Cassiopeia Medium Resolution – No Response Correction

## Slide 19: Kappa Cassiopeia High Resolution – No Response Correction

## Slide 20: The Allen Telescope University of London Observatory
  24” Richey-Chretien

## Slide 21: Kappa Cassiopeia Mill Hill Observatory 1993

## Slide 22: Processing a Spectrum Further Image Calibration
Cosmic ray removal
Flat fields
  Removes image artefacts dependent on the spectrum position on the imaging chip

## Slide 23: Processing a Spectrum Response Profile – Instrumental and Atmospheric Correction
Take a spectrum of a standard A type star
  Close to air mass (altitude) of the target star
Divide this by a professional reference spectrum of the same star
Smooth the resultant curve to remove minor artefacts
This is the response profile!
Used to correct the spectrum of the target star for your equipment and the Earth’s atmosphere

## Slide 24: Rho Persei Instrument and Atmospheric Response Corrected but no Flat Field
Red giant with a temperature of about 4000K and a semiregular variable star

## Slide 25: Kappa Cassiopeia Flat Field & Response Corrected

## Slide 26: Hydrogen Alpha Line B Stars in Cassiopeia
B Star Temperatures: 15,500K~28,000K

## Slide 27: Refining LHIRES III Setup Main Mirror Position
Adjusting the main mirror position on the LHIRES III to optimise the light throughput
Low
Middle
High

## Slide 28: Kappa Cassiopeia Optimising the Spectrograph
Adjusting LHIRES III mirror position
along with telescope and guide camera focus

## Slide 29: Shift in the Continuum
Over a 20 minute period the recorded continuum of the reference star has shifted.
I suspect this was due to sampling a shifting section of the star’s seeing disk which is subject to atmospheric dispersion.

## Slide 30: Atmospheric Dispersion
Atmospheric Dispersion
Difference parts of the seeing disc will preferentially contain stronger red of blue light from the star
Airy disc
Not a point source and will be subject to blurring by the atmosphere

## Slide 31: Chi Cygni Mira Type Variable
Low resolution response corrected

## Slide 32: Chi Cygni H-Alpha Mira Type Variable
High resolution response corrected

## Slide 33: AG Pegasi Symbiotic Star – Red Giant and White Dwarf
Low resolution response corrected

## Slide 34: AG Pegasi H-Alpha Symbiotic Star – Red Giant and White Dwarf
High resolution response corrected

## Slide 35: The Orion Nebula

## Slide 36: Vega High Resolution & Fully Calibrated

## Slide 37: Comet Lovejoy

## Slide 38: Processing a Spectrum Further Enhancements - Future Challenges!
Improved wavelength calibration
  Use telluric lines around H-Alpha
Flux calibration
  Gives the actual energy received from the star at different wavelengths
Removal of interstellar reddening
  Corrects the spectrum for the effects of interstellar dust that absorbs more blue light than red light

## Slide 39: Future Projects
Variable stars of all types
Radial velocity measurements
Galaxy rotation
Be stars
Detailed analysis of nebulae emission line

## Slide 40: Further Information
Wikimedia Commons used as source for many images:
http://commons.wikimedia.org/wiki/Main_Page
Spectroscopy Yahoo Groups
https://groups.yahoo.com/neo/groups/astronomical_spectroscopy/info
https://groups.yahoo.com/neo/groups/spectro-l/conversations/messages
ARAS – Astronomical Ring for Access to Spectroscopy
http://www.spectro-aras.com/forum/index.php
British Astronomical Association Variable Star Section
http://www.britastro.org/vss/
Online Astronomy Society Astronomical Spectroscopy Facebook Group
https://www.facebook.com/groups/362613490511970/
Me – Andy Wilson: barnards.star12@gmail.com